## Slide 1: Parallel mycavity
Pavan Govindaraju Emeric Boigne
ME 469 Project

## Slide 2: Objectives
Broad objective - Parallelizing mycavity
Two approaches
  CPUs - Pavan
  GPUs - Emeric

## Slide 3: Default Code Profile
3/4th of the time spent in sipsol
Number of calls = isteps(10) * timesteps(51)

## Slide 4: Objectives - CPUs
Use a more efficient solver
  Currently uses SIP - Iterative
Direct solver?
  Memory intensive (not for sparse-direct, but complex)
  Must complete for useful results
Using a distributed linear solver?
Objectives
  SuperLU - sequential sparse direct
  Full throttle : FGMRES - distributed sparse iterative

## Slide 5: SuperLU in mycavity
Support routines
  Armadillo (http://arma.sourceforge.net/) - interface between mycavity (C++) and SuperLU (C)
  Other supporting code - Sparse matrix class
Essentially replaced sipsol with sipsol_arma
Note that calcp() is NOT replaced with direct solver - extremely high condition number

## Slide 6: SuperLU - Results
Solve time (For 100x100 grid) per timestep
  SIP : 0.708s
  SuperLU : 2.91s 
Direct solvers are expensive as well
Note that this is NOT a banded matrix. The band size depends on the grid.
Also something dumb : Dense solver
  LAPACK : 1m 24s

## Slide 7: M(assivel)y-parallel cavity
Definitely utilize sparse structure for this problem
Elemental (http://libelemental.org/) is a C++ distributed memory linear algebra library. Maintained by Stanford faculty Jack Poulson
Encapsulates MPI calls and other matrix support routines
In-built distributed sparse linear solver uses modified GMRES with a preconditioner
Successfully scaled mycavity to 2048 cores (and counting)

## Slide 8: Elemental - Results
Solve time (For 100x100 grid) per timestep
  SIP : 0.708s , SuperLU : 2.91s 
  Elemental (1 core) : 0.431s 
Runtime test on NERSC Edison for 4000x4000 grid

## Slide 9: Mycavity - Strong scaling
Tests performed on NERSC Edison for 1000x1000 grid
Speedup still increases beyond this range

## Slide 10: Solver verification
First verified matrix structure and entries
  Linear problem correctly constructed!
Verified one linear solve is gives similar results
  This is checked for subsequent timesteps
  Linear solve correctly performed!
  Also field quantities correctly reassigned!
Finally, quantities of interest in mycavity.out are compared

## Slide 11: Summary
Best way to speed up the code is to replace the solver
Used support routines and specialized libraries to replace mycavity solver
Two solvers demonstrated
  SuperLU - sequential, sparse, direct
  Elemental - parallel, sparse, iterative
Strong scaling demonstrated. Code speedup observed upto 2048 cores

## Slide 12: References
Code is available on request(WiP) on GitHub https://github.com/gpavanb/mycavity
Poulson, Jack, et al. "Elemental: A new framework for distributed memory dense matrix computations." ACM TOMS 39.2 (2013): 13.
Li, Xiaoye S., et al. "SuperLU users’ guide.” Report, LBNL-44289 (1999).